ADDENDUM

Hole Spacing Error:

Figure 3 and step 4 on page 3 reference marking centerlines for the holes  9 1/8" from center.

9 1/8" x 2 is 18 1/4", not 19 1/4".  The holes should be 9 5/8" from center.

Thermostat Installation Instructions

In the fan tube you will find a blue wire nut. Remove that wire nut and separate the wires (two wires). The fan tube has a hole where you can pass the thermostat wire through to the inside of the tube. Connect the red and the white wire of the thermostat to those two wires and put the wire nuts back onto the wires. Note there is another wire nut provide in the kit. Using the same bay between the studs run the wire up the wall. Remove the front cover off the thermostat and you will see two terminals on the top of the thermostat that are marked W and RH. Connect the red and the white thermostat wires to those terminals. (Note) Poke a hole approximately 5 feet up the wall and run a snake down the wall; then attach the thermostat wire to the snake and pull the thermostat wire up the wall.